## Slide 1: GraphPulse An Event-Driven Hardware Accelerator for Asynchronous Graph Processing
Shafiur Rahman Nael Abu-Ghazaleh Rajiv Gupta
MICRO-53
October 21, 2020

## Slide 2: Growing Demand for Graph Analytics on Large Graphs
Graph algorithms are important computational workloads on many domains
  Social Networks
  Web graphs
  Brain networks
  Bioinformatics
Few types of algorithms are used in many important applications
  Centrality Analysis (e.g., PageRank)
  Path Finding (e.g., BFS, SSSP)
  Recommendation System (e.g. Adsorption)
  Community Detection (e.g., Connected Components)

## Slide 3: Graph Applications Have Poor Memory Locality
Vertex-Centric processing has inefficient memory access
  Irregular access pattern
  Dynamic data dependence
  Low computation-to-communication ratio
  Poor spatial and temporal locality
Software implementations are limited by memory system
- On-chip caches are too small to exploit locality

## Slide 4: Memory Access Patterns in Vertex-centric Processing
Example Graph
Sequential Read
Sequential Read
Random Write
Atomics
Pushing updates to outgoing neighbors requires random memory writes and atomic operations
≈ Expensive
Each vertex either Pushes or Pulls updates to/from neighbors

## Slide 5: Memory Access Patterns in Vertex-centric Processing
Example Graph
Pulling updates from incoming neighbors involves - Random memory reads and - Redundant reads of unmodified states
Each vertex either Pushes or Pulls updates to/from neighbors
Sequential Read
Random Read
Sequential Write

## Slide 6: Hardware Support for Graph Processing
Hardware-based frameworks improves performance by
  Using on-chip memory as large/dedicated cache
  Using specialized pipeline
  Providing primitives for efficient atomics operation
  Specialized scheduling policy
Hardware implementations following “Think-like-a-vertex” approach like software still suffers the same memory inefficiencies
  Limited control over memory access patterns
  Heavy dependence on graph structures
  Unable to take full advantage of the capabilities of the hardware.
Specialized execution model is necessary for best use of hardware capabilities

## Slide 7: Event-Driven Execution Concept
Idea:
Decouple the memory accesses from communication among vertices
Updates are queued as messages
Use the message for scheduling (message becomes events)
No separate active list maintenance
Fine-grained control over scheduling
Each vertex accesses its own properties only
Eliminates random reads of input set
Simplified memory access pattern
Simplified transaction-safety

## Slide 8: Event-Driven Processing Example (SSSP)
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Initial Vertex Properties
Initial Events
Reduce function
Propagate Function
Local Termination condition
User defines
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 9: Event-Driven Processing Example (SSSP)
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A
B
C
D
E
5
2
2
3
1
1
7
A, 0
Queue
Vertex Property
V[i] = ∞ (source, 0)
Initialization

## Slide 10: Event-Driven Processing Example (SSSP)
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
A, 0
Queue
Vertex Property
Min(x,y)
Update
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 11: Event-Driven Processing Example (SSSP)
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
A, 0
Queue
Vertex Property
Sum(x,y)
B, 5
C, 2
Propagate
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 12: Event-Driven Processing Example (SSSP)
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
B= 5
C= 2
A, 0
B, 5
C, 2
D, 8
B, 4
D, 9
Queue
Vertex Property
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Iterate
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 13: Event-Driven Processing Example (SSSP)
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
B= 5
C= 2
A, 0
B, 5
C, 2
D, 8
B, 4
D, 9
Queue
Vertex Property
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Iterate
D= 8
E, 9
B= 4
D, 7
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 14: Event-Driven Processing Example (SSSP)
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
B= 5
C= 2
A, 0
B, 5
C, 2
D, 8
B, 4
D, 9
Queue
Vertex Property
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Propagation Stops
D= 8
E, 9
B= 4
D, 7
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 15: Event-Driven Processing Example (SSSP)
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
B= 5
C= 2
A, 0
B, 5
C, 2
D, 8
B, 4
D, 9
Queue
Vertex Property
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Iterate
D= 8
E, 9
B= 4
D, 7
E= 9
C, 10
E, 8
D= 7
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 16: Event-Driven Processing Example (SSSP)
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
B= 5
C= 2
A, 0
B, 5
C, 2
D, 8
B, 4
D, 9
Queue
Vertex Property
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Iterate
D= 8
E, 9
B= 4
D, 7
E= 9
C, 10
E, 8
D= 7
E= 8
C, 9
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 17: Event-Driven Processing Example (SSSP)
A= ∞
B= ∞
C= ∞
D= ∞
E= ∞
A= 0
B= 5
C= 2
A, 0
B, 5
C, 2
D, 8
B, 4
D, 9
Queue
Vertex Property
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
Temp ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] < Temp then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Terminate
D= 8
E, 9
B= 4
D, 7
E= 9
C, 10
E, 8
D= 7
E= 8
C, 9
A
B
C
D
E
5
2
2
3
1
1
7

## Slide 18: Memory Access Pattern for Event-driven Processing
Eliminated random accesses of neighbor vertices
  Each vertex can access only its own data
Random Read
Random Write
Sequential Read
The reads/writes are still random
Parallel operations still require locking
Memory access is isolated to target vertex
Simpler locking/atomic operation
Graph structure doesn’t affect locality
Memory access pattern depends on scheduling only (not graph structure)

## Slide 19: Reducing Random Accesses
Reduce function is commutative and associative for many algorithms
Events can be processed in any order while maintaining correctness
  Allows flexible scheduling policy
Sorted Queue
Sequential Memory Access
Issuing events in sorted order removes random read/writes

## Slide 20: Event Population Control
Each processed event generates new events for all edges
  Event Generation Rate >> Event Consumption Rate
  Exponential growth of event population
  Extreme overhead to manage events
Solution: Coalesce events destined for same vertex
Chart: 
 | 68475391 | 68381956 | 67701547 | 67233784 | 66482281 | 65468640 | 64499845 | 63681429 | 62791672 | 61871081 | 60655756 | 59334670 | 57598693 | 54876252 | 50005392 | 42782506 | 34667993 | 23253058 | 8972258 | 1345995
Chart: 
 | 4471652 | 4461693 | 4441785 | 4433000 | 4428221 | 4407464 | 4406474 | 4381832 | 4382235 | 4347243 | 4340082 | 4283823 | 4259991 | 4146714 | 4016198 | 3680378 | 3219000 | 2454494 | 1242000 | 224260
coalesce
4.84M
vertices
68.9M edges
#events bounded by #edges
#events bounded by #vertices
Total events generated in each iteration [PageRank in LiveJournal graph]
Total events remaining after coalescing

## Slide 21: Event Coalescing
Propagate functions are distributive for many algorithms
Multiple events for same vertex can be merged using the Reduce function
  Makes total number of events in the queue bounded by number of vertices
Only one event for each vertex exists in the queue at a moment
  Guarantees contention-free scheduling [Parallel execution without locking]
  Reduced storage for events
  Less number of processing tasks
  Implicit guarantee of transaction-safety
  Approaches convergences faster
Benefits from Coalescing

## Slide 22: Graph Properties for Event-driven Processing
Reordering Property
  Reduce function must be commutative, associative and distributive
  Propagate function must be distributive over Reduce function
Reordering property allows events to be sorted and coalesced
Simplification Property
  A vertex should not have impact on its neighbors if it doesn’t change
Simplification property allows events to stop propagation and terminate the algorithm
Reduce functions
Propagate functions
Algorithms
Sum,
Product,
Min, Max,
And, Or,
1-hot
Sum,
Product,
Min, Max,
And, Or
Incremental PageRank,
Adsorption, SimRank,
SSSP, BFS, HITS
Connected Components,
Linear Equation Solver
Examples

## Slide 23: Hardware Acceleration of Event-Driven Execution
Sorted Queue implementation is expensive in software
Coalescing within a queue has huge overhead
Event scheduling policy implementations may be inefficient
Challenges
GraphPulse is an asynchronous graph processing accelerator that leverages the decoupling of vertex updates and vertex communications to maximize memory access efficiency and increase parallelism.
GraphPulse provides hardware primitives to mitigate these challenges

## Slide 24: GraphPulse Architecture
Event Queue with in-place coalescing
  Direct-mapped storage for events
  Coalesces events during insertion
  Multiple bins for parallel insertion/issue
  Adjacent vertices in queue are also adjacent in off-chip graph memory
bins
  Fast insertion/issue of events
  Efficient in-place coalescing

## Slide 25: GraphPulse Architecture
Event Scheduler
  Get events in bulk from queue
  Buffers events from queue to minimize idle-time
  Schedules memory-adjacent vertices to one processor
  Memory-access friendly scheduling
  Maximize parallelism

## Slide 26: GraphPulse Architecture
Event Processors
  Events indicates the vertices to be accessed
  Target vertices can be accurately prefetched
  Prefetcher optimizes DRAM page accesses and skips unnecessary DRAM row reads
  Parallel event generation units for saturating DRAM bandwidth
  Accurate prefetching
  Optimize memory bandwidth utilization

## Slide 27: Evaluated Systems
Cycle-accurate hardware simulation based on Structural Simulation Toolkit
  8x GraphPulse cores @1GHz
  64MB on-chip memory
Software Simulation in Ligra
  12-core Intel Xeon processor
  12MB L2 cache
  4-channel DDR3 with 17GB/s
Five Graph processing algorithms
  Incremental PageRank
  Single-source Shortest Path
  Breadth-first Search
  Adsorption
  Connected Components
Five real-world graphs
  Google Web Graph
  Facebook Social Network
  Wikipedia Page Links
  LiveJournal Social Network
  Twitter Follower Graph
Graphicionado Hardware Accelerator
  8x Graphicionado pipelines @1GHz
  64MB on-chip memory

## Slide 28: Performance
Chart: Speedup over Ligra
| WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | PageRank-Delta | Adsorption | Single Source Shortest Path | Breadth-first Search | Connected Components
GraphPulse | 36.96 | 39.16 | 73.87 | 39.19 | 57.44 | 45.85 | 11.21 | 19.83 | 55.45 | 22.21 | 39.06 | 21.9 | 21.75 | 48.55 | 37.28 | 10.84 | 22.6 | 21.75 | 35.48 | 31.27 | 26.73 | 26.92 | 32 | 30.13 | 29.77 | 55.48 | 45.58 | 17.41 | 48.39 | 32.97
Graphicionado | 6.38 | 13.42 | 4.38 | 7.34 | 6.28 | 6.62 | 1.6 | 3.61 | 14.5 | 3.42 | 3.1 | 3.89 | 4.54 | 10.35 | 7.32 | 1.68 | 4.02 | 3.86 | 8.11 | 5.9 | 4.62 | 5.07 | 3.55 | 5.25 | 4.35 | 4.51 | 3.54 | 1.62 | 3.48 | 3.3
GraphPulse achieves ~28x speedup over state-of-the-art software framework
and ~6.2x speedup over hardware accelerator.

## Slide 29: Reduced off-chip memory access
GraphPulse requires ~54% less off-chip accesses compared to optimized hardware accelerator with conventional processing
Chart: Total off-chip memory access normalized to Graphicionado
| WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | PageRank-Delta | Adsorption | Single Source Shortest Path | Breadth-first Search | Connected Components
Off-chip access | 0.39 | 0.35 | 0.53 | 0.65 | 0.53 | 0.48 | 0.35 | 0.4 | 0.48 | 0.62 | 0.54 | 0.47 | 0.53 | 0.59 | 0.59 | 0.64 | 0.54 | 0.58 | 0.55 | 0.7 | 0.66 | 0.66 | 0.68 | 0.65 | 0.31 | 0.24 | 0.22 | 0.25 | 0.2 | 0.24

## Slide 30: Efficient utilization of transferred data
GraphPulse utilizes ~75% of accessed data in useful computation as result of accurate prefetching and memory-optimized scheduling
Chart: Utilization factor of off-chip data
| WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | WG | FB | WK | LJ | TW | AVG | PageRank-Delta | Adsorption | Single Source Shortest Path | Breadth-first Search | Connected Components
Utilization | 0.72 | 0.98 | 0.82 | 0.96 | 0.9 | 0.87 | 0.54 | 0.82 | 0.7 | 0.77 | 0.74 | 0.71 | 0.43 | 0.88 | 0.69 | 0.84 | 0.84 | 0.71 | 0.49 | 0.8 | 0.71 | 0.76 | 0.73 | 0.69 | 0.74 | 0.98 | 0.84 | 0.95 | 0.91 | 0.88

## Slide 31: See paper for more…
Architecture details
Details on the event-driven execution model
Partitioning and scaling methods
More evaluation results
ASIC Area and energy estimates

## Slide 32: Conclusion
Event-driven processing eliminates major memory bottlenecks in graph analytics
  Fine-grained control over scheduling
  Lock-free memory access for extensive parallelism
  Hardware-friendly abstraction
GraphPulse provides an efficient architecture for event-driven graph processing
  Allows efficient event-coalescing to control event-population and faster convergence
  Optimized prefetching saturates memory bandwidth
  Efficient memory access pattern for maximum utilization of DRAM accesses
Evaluation demonstrates the advantage of GraphPulse
  28x performance improvement and 280x energy reduction on average

## Slide 33
This presentation and recording belong to the authors. No distribution is allowed without the authors' permission.
Thank You For Watching
Please contact the authors for question:
mrahm008@ucr.edu