## Slide 1
Shafiur Rahman Mahbod Afarin Nael Abu-Ghazaleh Rajiv Gupta
JetStream Graph Analytics on Streaming Data with Event-driven Hardware Accelerator
MICRO 2021

## Slide 2: Streaming Graph Processing
Real-world graphs changes rapidly over time
Reevaluation of full graph is computationally expensive
  Many vertices are not affected by the change
Full
Computation
Query
Full
Computation
Query
edge addition,
deletion

## Slide 3: Incremental Recomputation
Full
Computation
Query
Incremental
Computation
Query
edge addition,
deletion
approximate
states
Reuse vertex states from previous evaluation
Approximate states for the initial states of new evaluations
  Faster convergence
  Reduced Computation

## Slide 4: Event-Driven Execution Concept
Decouple the memory accesses from communication among vertices
Updates are queued as messages
Use the message for scheduling (message becomes events)
No separate active list maintenance
Fine-grained control over scheduling
Each vertex accesses its own properties only
Eliminates random reads of input set
Simplified memory access pattern
Simplified transaction-safety

## Slide 5: Event-Driven Processing Example (SSSP)
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
Initial Vertex Properties
Initial Events
Reduce function
Propagate Function
Local Termination condition
User defines

## Slide 6: Event-Driven Processing Example (SSSP)
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
V[i] = ∞ (source, 0)
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
Queue
Initialize Events
Initialize Vertices

## Slide 7: Event-Driven Processing Example (SSSP)
Min(x,y)
Update
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
Queue
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13

## Slide 8: Event-Driven Processing Example (SSSP)
Sum(x,y)
Propagate
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
7
3
8
12
5
13
8
0
12
5
3
8
Queue
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
B
7
C
3
D
8

## Slide 9: Event-Driven Processing Example (SSSP)
Iterate
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
7
3
8
12
5
B
7
C
3
D
8
8
0
12
5
3
8
Queue
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
E
14
B
5
D
9
E
13

## Slide 10: Event-Driven Processing Example (SSSP)
Coalesce
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
7
3
8
12
5
B
7
C
3
D
8
E
14
B
5
D
9
E
13
8
0
12
5
3
8
Queue
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
E
14
E
13
E
13
Min()

## Slide 11: Event-Driven Processing Example (SSSP)
Iterate
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
7
3
8
12
5
B
7
C
3
D
8
E
13
B
5
D
9
13
8
0
12
5
3
8
Queue
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
C
15
E
12

## Slide 12: Event-Driven Processing Example (SSSP)
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
7
3
8
12
5
B
7
C
3
D
8
E
14
B
5
D
9
C
15
13
E
12
8
0
12
5
3
8
Queue
Vertex value unchanged Propagation Stops
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13

## Slide 13: Event-Driven Processing Example (SSSP)
Iterate
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
7
3
8
12
5
B
7
C
3
D
8
E
14
B
5
D
9
C
15
13
E
12
8
0
12
5
3
8
Queue
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13
3

## Slide 14: Event-Driven Processing Example (SSSP)
Terminate
A
B
C
D
E
7
3
2
7
5
2
8
6
A
0
A
E
B
C
D
∞
∞
∞
∞
∞
0
7
3
8
12
5
B
7
C
3
D
8
E
14
B
5
D
9
C
15
13
E
12
8
0
12
5
3
8
Queue
3
Queue Empty
V[:] ← InitialVertexProperty(V)
Queue ← InitialEvents(V)
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
12
13

## Slide 15: Event-Based Processing for Streaming Graph
Decoupled Model
  Isolates computation from communication (graph structure)
  Graph mutations do not affect memory access pattern
Asynchronous Computation
  Easier to represent streaming operations with reorderable computation model
Changes in graph structure can be encoded in events
Benefits for Streaming Graphs
Translates into robust high performance hardware implementation

## Slide 16: Event Representation of Edge Addition
A
B
C
D
E
7
3
2
7
5
2
8
6
5
E
12  5
C
7
3  3
Event-driven execution is asynchronous
  Events can be processed in any order
An added edge is equivalent to an event processed late
5
Edge addition event
A
B
C
D
E
7
3
8
B
∞  0
∞  7
∞  8
∞  3
∞  13
13
E
14
13  13
D
C
3  3
15
8  8
7  5
E
12
13  12
C
14
3  3
initial event
A | B | C | D | E
Expected Values |  |  |  | 
0 | 5 | 3 | 8 | 5
New Values |  |  |  | 
0 | 5 | 3 | 8 | 5

## Slide 17: Processing an Edge Addition
foreach added edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
1
2
3
4
E
5
A
E
B
C
D
13
0
12
5
3
8
Queue
3
Process Edge Additions
A
B
C
D
E
7
3
2
7
5
2
8
6
5

## Slide 18: Processing an Edge Addition
foreach added edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
1
2
3
4
E
5
A
E
B
C
D
5
0
12
5
3
8
Queue
3
Process Edge Additions
A
B
C
D
E
7
3
2
7
5
2
8
6
5
0
5
5
3
8
C
7
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
Regular Computation

## Slide 19: Event Representation of Edge Deletions
Edge deletions are more complex to handle
A deleted edge already carried updates through it
  The affected vertices remain in incorrect state
  The updates through a deleted edge must be reverted
A
B
C
D
E
7
3
8
B
∞  0
∞  7
∞  8
∞  3
∞  13
13
E
14
13  13
D
C
3  3
15
8  8
7  5
E
12
13  12
C
14
3  3
initial event
A
B
C
D
E
7
3
2
7
5
2
8
6

## Slide 20: Event Representation of Edge Deletions
A
B
C
D
E
7
3
2
7
5
2
8
6
Reduce (Apply) function is monotonic
  Vertex value cannot revert from an event.
Vertex must be reset, so that new events can update it
A
B
C
D
E
7
3
8
B
∞  0
∞  7
∞  8
∞  3
∞  13
13
E
14
13  13
D
C
3  3
15
8  8
7  5
E
12
13  12
C
14
3  3
initial event
C
3  3
∞
Edge deletion event
A | B | C | D | E
Expected Values |  |  |  | 
0 | 7 | 15 | 8 | 13
Computed Values |  |  |  | 
0 | 5 | 3 | 8 | 12
3  ∞

## Slide 21: Event Representation of Edge Deletions
A
B
C
D
E
7
3
2
7
5
2
8
6
Resetting the destination vertex is not enough
  Other impacted vertices will not revert
All vertices impacted by this edge must be reset
A
B
C
D
E
7
3
8
B
∞  0
∞  7
∞  8
∞  3
∞  13
13
E
14
13  13
D
C
3  3
15
8  8
7  5
E
12
13  12
C
14
3  3
initial event
C
3  ∞
∞
Edge deletion event
A | B | C | D | E
Expected Values |  |  |  | 
0 | 7 | 15 | 8 | 13
Computed Values |  |  |  | 
0 | 5 | ∞ | 8 | 12
B
D
8  8
5  5
∞
∞

## Slide 22: Recovery Approach – Vertex Tagging
A | B | C | D | E
Previous Values |  |  |  | 
0 | 5 | 3 | 8 | 12
After Recovery |  |  |  | 
0 | ∞ | ∞ | ∞ | ∞
C
∞
B
3  ∞
D
8  ∞
5  ∞
E
∞
12  ∞
C
∞
∞  ∞
∞
∞
E
∞
∞  ∞
Separate Recovery Phase to reset all impacted vertices
Propagate a tag to all neighbors from an impacted vertex
  Tagged vertices will reset themselves and propagate tag
  Tag propagation stops when a vertex is already tagged
New events can restore reset vertices to correct state
A
B
C
D
E
7
3
2
7
5
2
8
6
delete event

## Slide 23: Reapproximation After Edge Deletion
B
C
D
E
7
∞
8
∞  7
∞  8
∞  ∞
∞  13
13
E
14
13  13
C
∞  15
15
E
∞
∞  ∞
B
D
8  8
7  7
17
21
A | B | C | D | E
Expected Values |  |  |  | 
0 | 7 | 15 | 8 | 13
Approximation |  |  |  | 
0 | 7 | 15 | 8 | 13
A | B | C | D | E
After Recovery |  |  |  | 
0 | ∞ | ∞ | ∞ | ∞
Reapproximation
Events
Reset vertices need new events to converge
Create new events from all incoming neighbors
  Tagged vertex requests updates from neighbors
  Neighbor vertices propagate their states
Reapproximation events restores the correct vertex states
A
B
C
D
E
7
3
2
7
5
2
8
6
E
B
∞
∞  ∞
C
A
A
D
∞  ∞
C
∞
B
E
∞  ∞
D
∞
Evaluate query on this approximation for correct result

## Slide 24: Processing a Deleted Edge
A
B
C
D
E
7
3
2
7
5
2
8
6
foreach deleted edge E(u,v) do
Queue ← insert(v, ∞)
end
1
2
3
Process Edge Deletions
C
∞
A
E
B
C
D
5
0
12
5
3
8
Queue
3

## Slide 25: Recovery from a Deleted Edge
A
B
C
D
E
7
3
2
7
5
2
8
6
foreach deleted edge E(u,v) do
Queue ← insert(v, ∞)
end
1
2
3
Process Edge Deletions
C
∞
A
E
B
C
D
0
12
5
3
8
Queue
∞
0
∞
∞
∞
∞
B
∞
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Δ
if oldVal != Δ then
foreach outgoing edge E(u,v) do
Queue ← insert(v, Δ)
end
end
end
1
2
3
4
5
6
7
8
9
10
Recovery
∞
E
∞
D
∞
∞
E
∞
∞
∞
∞

## Slide 26: Recovery from a Deleted Edge
A
B
C
D
E
7
3
2
7
5
2
8
6
foreach deleted edge E(u,v) do
Queue ← insert(v, ∞)
end
1
2
3
Process Edge Deletions
C
∞
A
E
B
C
D
0
12
5
3
8
Queue
∞
0
∞
∞
∞
∞
B
∞
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Δ
if oldVal != Δ then
foreach outgoing edge E(u,v) do
Queue ← insert(v, Δ)
end
end
end
1
2
3
4
5
6
7
8
9
10
Recovery
∞
E
∞
D
∞
∞
E
∞
∞
C
∞
∞
∞

## Slide 27: Recomputation after Recovery
A
B
C
D
E
7
2
7
5
2
8
6
foreach impacted vertex I do
foreach incoming edge E(u,v) of I do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
1
2
3
4
5
Reapproximate Vertex States
B
7
A
E
B
C
D
Queue
0
∞
∞
∞
∞
B
∞
C
∞
D
8
D
∞
E
∞
E
∞

## Slide 28: Recomputation after Recovery
A
B
C
D
E
7
2
7
5
2
8
6
foreach impacted vertex I do
foreach incoming edge E(u,v) of I do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
1
2
3
4
5
Reapproximate Vertex States
B
7
A
E
B
C
D
Queue
0
∞
∞
∞
∞
B
∞
C
∞
D
8
D
∞
E
∞
E
∞
Coalesce

## Slide 29: Recomputation after Recovery
A
B
C
D
E
7
2
7
5
2
8
6
foreach impacted vertex I do
foreach incoming edge E(u,v) of I do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
1
2
3
4
5
Reapproximate Vertex States
B
7
A
E
B
C
D
Queue
0
∞
∞
∞
∞
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
Regular Computation
C
∞
D
8
E
∞
7
8
∞
E
14
E
13

## Slide 30: Recomputation after Recovery
A
B
C
D
E
7
2
7
5
2
8
6
foreach impacted vertex I do
foreach incoming edge E(u,v) of I do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
1
2
3
4
5
Reapproximate Vertex States
B
7
A
E
B
C
D
Queue
0
∞
∞
∞
∞
while Queue is not empty do
(u, Δ) ← pop(Queue)
oldVal ← V[u]
V[u] ← Reduce(V[u], Δ)
if V[u] != oldVal then
foreach outgoing edge E(u,v) do
Δv ← Propagate(V[u], E.wgt)
Queue ← insert(v, Δv)
end
end
end
1
2
3
4
5
6
7
8
9
10
11
Regular Computation
C
∞
D
8
E
13
15
7
8
13
∞
C
15
B
7
D
8
7
8
0
13
∞
15
8

## Slide 31: Selective vs Accumulative Algorithms
Selective algorithms
  Reduce function keeps only one value (Min, Max, AND, OR)
  Monotonic Nature
  Only one edge contributes to the final value of a vertex
  BFS, SSSP, SSSP, Connected Components, etc.
Accumulative Algorithms
  Reduce function accumulates values (Sum, Product)
  All active edge contributes to the value of a vertex
  PageRank, Adsorption, etc.
Non-monotonic: Edge deletion is equivalent to edge addition
Deletion events can revert effects of the deleted edge
Do not need separate recovery phase
Features of Accumulative algorithms

## Slide 32: Hardware Acceleration of Incremental Recomputation
GraphPulse is an asynchronous graph processing accelerator that leverages the decoupling of vertex updates and vertex communications to maximize memory access efficiency and increase parallelism.
GraphPulse provides hardware primitives to mitigate challenges of Event-Driven Execution
Implements sorted queue which has high complexity in software
Enables coalescing within a queue without extra overhead
Implements low-cost event scheduling policy
Features
JetStream extends GraphPulse for Streaming Graphs

## Slide 33: JetStream Base Architecture
Event Queue
  In-place coalescing of events
  Events sorted by destination
  Fast insertion and issue of events
Event Scheduler
  System-level control
  Memory access friendly scheduling
  Fetch, buffer, and issue events
  Maximize parallelism
Event Processors
  Accurate prefetching of target vertices
  Optimize DRAM reads with prefetcher
  Event generation in parallel
Abstract view of the JetStream Base Architecture (GraphPulse)

## Slide 34: GraphPulse Original Datapath
(host initializes vertex data and event)
Read initial event to queue
a. Request events from queue
b. Queue emit events
(loop)
Issue events to available processor
Prefetches vertex properties
Apply vertex update
(Writeback to scratchpad)
Send to generation units
Prefetches edge list
Generates events (Propagate)
Events routed through event bus
Queue picks up events from bus
Typical Compute phase – Continues until queue is empty
0
0
1
1
1
1
2
3
2
3
4
5
4
5
6
7
8
9
6
7
8
9

## Slide 35: Architectural Extensions for JetStream
Reset Logic
Stream Reader
Reads list of modified edges
Sends to scheduler for creating events
Impact Buffer
Records list of impacted edges
Stores to and fetches from DRAM
Scheduler
Extended to handle multiple phase and creation of streaming events
Reset Logic
Apply unit extended for vertex reset from edge deletions
Coalescer
Extended to coalesce delete events
NoC
Expanded to handle larger event size

## Slide 36: JetStream Execution Flow
Reset Logic
2
3
4
5
7
8
9
Stream Events Creation
Read streamed edges from list
A
A
Pass edges through scheduler
2
Read source vertex value
3
Create and insert event
9
4
5
8
7

## Slide 37: JetStream Execution Flow
Reset Logic
Recovery From Deleted Edges
Typical Compute Cycle using Reset Logic
9
Record impacted edges
B
1
B

## Slide 38: JetStream Execution Flow
Reset Logic
2
3
4
5
7
8
9
Reapproximation of Impacted Vertices
Read list of impacted vertices
C
C
Pass vertices through scheduler
2
Read input edge pointers
3
Create request events
9
4
5
8
7
Finally, run Compute Cycle for result
9
1
6
6

## Slide 39: Evaluated Systems
Cycle-accurate hardware simulation of GraphPulse and JetStream
  Based on Structural Simulation Toolkit
  8x GraphPulse cores @1GHz
  4x DDR3 17GB/s Channels
  64MB on-chip memory
Hardware Simulation
KickStarter for selective update algorithms and GraphBolt for accumulative update algorithms
  36x Intel Core i9 processors @3GHz
  24MB L2 Cache
  4x DDR4 19GB/s Channels
Software Systems

## Slide 40: Evaluated Workloads
Six heavily-used graph processing applications
  Incremental PageRank
  Adsorption
  Breadth-First Search
  Single-source Shortest Path
  Single-source Widest Path
  Connected Components
Graph Algorithms
Five real-world graph workloads
  Wikipedia Page Links (Wk)
  Facebook Social Network (FB)
  LiveJournal Social Network (LJ)
  .uk Domain Web Crawl - 2002 (UK)
  Twitter Follower Graph (TW)
Input Graphs

## Slide 41: JetStream Performance
Chart: Speedup over GraphPulse and KickStarter
| WK | FB | LJ | UK | TW | WK | FB | LJ | UK | TW | WK | FB | LJ | UK | TW | WK | FB | LJ | UK | TW | Geo. | Single-Source Widest Path | Single-Source Shortest Path | Breadth-First Search | Connected Components | Mean
Full Computation on GraphPulse | 10.4 | 9.3 | 16.7 | 66.7 | 43.2 | 9.4 | 9.95 | 13.3 | 73.4 | 35.5 | 3.1 | 5.35 | 7.8 | 8.18 | 15.1 | 12.9 | 13.2 | 12.4 | 21.4 | 23.4 | 14.8019
Incremental Computation on KickStarter | 12.4 | 13.1 | 8.4 | 24.2 | 5.2 | 21.8 | 8.7 | 6.5 | 25.6 | 11.2 | 30.1 | 8.31 | 11.7 | 11.5 | 5.57 | 7.62 | 8.6 | 5.25 | 9.38 | 8.51 | 10.5862
JetStream achieves ~10x speedup over KickStarter’s incremental reevaluation
and ~15x speedup over complete reevaluation in GraphPulse
for algorithms with Selective Updates.

## Slide 42: JetStream Performance
Chart: Speedup over GraphPulse and GraphBolt
| WK | FB | LJ | UK | TW | WK | FB | LJ | UK | TW | Geo. | PageRank | Adsorption | Mean
Full Computation on GraphPulse | 12.8 | 19.5 | 19.9 | 56.6 | 9.7 | 5.78 | 3.9 | 5.08 | 5.95 | 9.41 | 10.5746
Incremental Computation on GraphBolt | 143 | 231 | 180 | 402 | 51.6 | 12.7 | 14.4 | 15.9 | 12.8 | 38.6 | 53.0696
JetStream achieves ~53x speedup over GraphBolt’s incremental reevaluation
and ~10x speedup over complete reevaluation in GraphPulse
for algorithms with Accumulative Updates.

## Slide 43: JetStream Incremental Computation Efficiency
JetStream requires less than 7% of vertex computation compared to GraphPulse for incremental computation of a mutated graph
Chart: Vertex Computation Normalized to GraphPulse
| FB | WK | LJ | UK | FB | WK | LJ | UK | FB | WK | LJ | UK | FB | WK | LJ | UK | FB | WK | LJ | UK | Single-Source Widest Path | Single-Source Shortest Path | Breadth-First Search | Connected Components | PageRank
Vertex | 0.078873 | 0.066689 | 0.021663 | 0.015225 | 0.089724 | 0.0469 | 0.02885 | 0.019653 | 0.14033 | 0.21994 | 0.048893 | 0.020282 | 0.38141 | 0.53755 | 0.49762 | 0.22533 | 0.048959 | 0.057052 | 0.026477 | 0.01019

## Slide 44: JetStream Recovery Efficiency
JetStream’s delete propagation technique finds a smaller set of impacted vertices for most cases compared to KickStarter
Chart: Number of Vertices Reset by 30K Edge Deletion
| FB | WK | LJ | UK | TW | FB | WK | LJ | UK | TW | FB | WK | LJ | UK | TW | FB | WK | LJ | UK | TW | Single-Source Widest Path | Single-Source Shortest Path | Breadth-First Search | Connected Components
JetStream | 4926 | 6330 | 12979 | 12718 | 2787 | 12676 | 7532 | 11025 | 11465 | 2145 | 10411 | 24920 | 7393 | 74143 | 1348 | 26143 | 12987 | 16260 | 14709 | 7583
KickStarter | 10507 | 4553 | 17575 | 26772 | 2165 | 14918 | 13349 | 15346 | 23563 | 1650 | 5456 | 3866 | 4838 | 20894 | 1537 | 28274 | 18913 | 20492 | 17828 | 8729
74K

## Slide 45: JetStream Performance with Different Batch Sizes
JetStream performance increases significantly for smaller batch sizes. Speedup is more significant than KickStarter and GraphBolt.
Chart: Batch Size
| 100K | 10K | 1000 | 100 | 10
JetStream | 1 | 13.1579 | 357.1429 | 2100.8403 | 18181.8182
KickStarter | 0.13233 | 0.35922 | 0.63444 | 0.89831 | 2.2432
Chart: Batch Size
| 100K | 10K | 1000 | 100 | 10
JetStream | 1 | 2.6242 | 33.7134 | 80.7478 | 662.132
GraphBolt | 0.0065349 | 0.0071061 | 0.007651 | 0.0080134 | 0.0095797
Sensitivity to Batch Size

## Slide 46: Find More in Paper
Difference in execution methods for accumulative algorithms
Optimizations for delete propagations
  Value Aware Propagation Technique
  Dependency Aware Propagation Technique
More evaluations and sensitivity analysis
Power and area analysis

## Slide 47: Summary
Incremental processing for streaming graphs
  Capable of processing edge deletions
  Reuses data and reduces evaluation cost
Adopts event-driven techniques for efficient incremental evaluation
  Based on GraphPulse event-driven architecture
  Extension retains original functionalities
Significant improved performance for incremental computation
  13x speedup over complete recomputation in hardware accelerator
  18x speedup over incremental recomputation in software frameworks

## Slide 48: Thank You
This presentation and recording belong to the authors. No distribution is allowed without the authors' permission.
Please contact the authors for question
mrahm008@ucr.edu